## Slide 1
VIrtual Twins as tools for personalised clinicAL care
Postgraduate Training School #2
University of Auckland, Feb 9-12, 2026
Cardiovascular System Modelling
& Context of Use:
When, Why, and How Complex?
Dr Beatrice Ghitti [beatrice.ghitti@auckland.ac.nz]
Dr Finbar Argus [finbar.argus@auckland.ac.nz]

## Slide 2: Outline
PART I: CVS modelling & Context of use
Why do we need modelling “simplifications”?
Context of use
PART II: What options do we have?
From 3D to 1D models
Hetero-dimensional models & Geometric multiscale
PART III: Does one size fit all?
Sensitivity analysis
Identifiability analysis
& Model calibration in a nutshell

## Slide 3: PART I: CVS modelling & Context of use
“From experimental and clinical data acquisition to the personalisation of physiological models, […] to build a complete workflow for constructing cardiovascular digital twins, with applications to in-silico clinical trials, hypotheses testing, biomarker discovery, and more.”
What are the challenges of constructing and personalising complex and comprehensive physiological and computational models, and of using them, for instance, in clinical settings?
WHY do we need “simplifications”?

## Slide 4: CVS modelling & Context of use
Limited data or with noise
Computational complexity (vs clinical timeframes)
Parameter identifiability
?
??
???
What are the challenges of constructing and personalising complex and comprehensive physiological and computational models, and of using them, for instance, in clinical settings?
WHY do we need “simplifications”?

## Slide 5: CVS modelling & Context of use
WHAT do we need to simplify?
Function/physiology
Anatomy
WHERE do we need to simplify?
What districts of the system?
What spatial scales?
HOW can we simplify in a mathematically and biologically/physiologically valid way?
WHO?
Modellers and clinicians!
WHEN do we need to simplify?
These choices are guided by the specific applications / scientific questions to answer / physiological hypotheses to test
…the context of use of the model!

## Slide 6: CVS modelling & Context of use
💡 a context of use a CVS model
A simplified circulatory system model2
ADAVN model1
Anatomical complexity/simplification & Personalisation
Model reduction and Hetero-dimensional models
Interactions with other systems
Model sophistication for
biological mechanisms
mechanical characteristics
Accuracy vs Computational cost (time-sensitive clinical applications)
Physiological personalization

## Slide 7: CVS modelling & Context of use
💡🤔 Now, think of your context of use and keep it in mind…

## Slide 8: CVS modelling & Context of use
💡 a context of use a CVS model
Model reduction and Hetero-dimensional models

## Slide 9: CVS modelling & Context of use
3D models
1D models
0D models
Accuracy
Computational cost
💡 a context of use a CVS model
Geometric multi-scale modelling approach
Model reduction and Hetero-dimensional models

## Slide 10: PART II: Geometric multiscale – what options do we have?
3D models
1D models
0D models
Accuracy
Computational cost

## Slide 11: PART II: Geometric multiscale – what options do we have?
3D models
1D models
0D models
Accuracy
Computational cost
surrogates
High-fidelity models
Low-fidelity models

## Slide 12: Geometric multiscale – what options do we have?
3D models
1D models
0D models
Accuracy
Computational cost
3D models:
Resolve local details;
Account for blood flow features (blood rheology, velocity vectors, wall shear stresses, interaction between blood flow and vessel wall deformation);
Investigate the eﬀects of geometry.
Plaque formation, aneurysm formation, valve dysfunction, testing of medical devices (e.g., stents),…

## Slide 13: Geometric multiscale – what options do we have?
3D models
1D models
0D models
Accuracy
Computational cost
1D models:
Describe and analyse flow patterns, pressure wave propagation and reflection, average velocities in networks of vessels;
Compute local and global pulse wave velocity (PWV);
Offer good trade-off between accuracy and computational cost in simulating systemic hemodynamics.

## Slide 14: Geometric multiscale – what options do we have?
3D models
1D models
0D models
Accuracy
Computational cost
0D models:
Simulate global hemodynamics in the whole system, via spatially-homogeneous fields within any 0D compartment;
Provide BCs to 1D/3D models;
Have physical parameters usually quantifiable from clinical measurements.

## Slide 15: 3D Navier-Stokes equations of fluid dynamics
Three-dimensional (3D), time-dependent, nonlinear, incompressible Navier-Stokes equations (PDEs) describing the motion of a viscous fluid (blood):
with
: the domain of interest (the lumen of the vessel/system of vessels)
: fluid velocity vector field; : pressure scalar field
: blood density (constant); : blood dynamic viscosity (constant for Newtonian fluid model)
: external forces (gravity,…)
 : diffusive term
: nonlinear convective term
Reynolds number : ( diameter, mean sectional velocity)
Notes: Navier-Stokes eqs: balance of momentum = inertial forces + pressure forces + viscous forces
Conservation of mass / continuity eq (under incompressibility assumption)

## Slide 16: 3D Navier-Stokes equations of fluid dynamics
Three-dimensional (3D), time-dependent, nonlinear, incompressible Navier-Stokes equations (PDEs) describing the motion of a viscous fluid (blood):
with
: the domain of interest (the lumen of the vessel/system of vessels)
: fluid velocity vector field; : pressure scalar field
: blood density (constant); : blood dynamic viscosity (constant for Newtonian fluid model)
: external forces (gravity,…)
 : diffusive term
: nonlinear convective term
Reynolds number : ( diameter, mean sectional velocity)
Computational Fluid Dynamics (CFD)
Fluid-Structure Interaction (FSI) approach
Navier-Stokes equations of fluid dynamics (blood), coupled with
Equations of solid mechanics for the 3D structure (deformable vessel wall), via BCs.
Notes: Navier-Stokes eqs: balance of momentum = inertial forces + pressure forces + viscous forces
Conservation of mass / continuity eq (under incompressibility assumption)

## Slide 17: 1D averaged blood flow model
Several ways of deriving a one-dimensional (1D) model of an incompressible fluid flowing in a compliant pipe.
[see Formaggia, Quarteroni & Veneziani, Eds, (2009), doi: 10.1007/978-88-470-1152-6]
Asymptotic analysis on the 3D incompressible Navier-Stokes equations, by assuming and discarding the higher order terms in to simplify the equations.
Integrating the Navier-Stokes equations on a generic section, by assuming cylindrical symmetry.
Making use of the Reynolds’ transport theorem, to derive the 1D mass conservation and momentum balance equations.
 More general approach, no simplifying assumptions on the vessel section geometry.

## Slide 18: 1D averaged blood flow model
One-dimensional (1D) blood flow equations (PDEs) in a deformable vessel:
with
: vessel cross-sectional area; : flow rate; : cross-sectional averaged internal pressure
Assumed axisymmetric velocity profile
: average fluid velocity on a cross-section
: momentum correction factor; : blood density (constant); : viscous resistance coefficient
: vessel length
…we have 2 equations in 3 unknowns (, , and )!!!
Notes: Balance of momentum eq = convective term + pressure gradient + friction force per unit length
Mass conservation eq / continuity eq

## Slide 19: 1D averaged blood flow model
To close the system, we need to introduce a constitutive equation that characterizes the vessel wall behaviour  a pressure-area relation (or tube law).
Example: simple constitutive equation for the vessel wall under the assumption of linear elastic incompressible behaviour in arteries
with
: reference area and pressure; : reference radius
: wall thickness
: Young elastic modulus
: Poisson ratio ( for incompressible material)
In general
elastic component
viscoelastic component (Voigt-type)
: vessel wall stiffness parameter
More details in tomorrow’s lecture on constitutive modelling by A. Giudici!!!

## Slide 20: Pulse wave velocity (PWV)
: wall compliance per unit of vessel length
: local PWV – a measure of arterial stiffness
OR global PWV : cf-PWV (carotid-femoral), ba-PWV (brachial-ankle),…

## Slide 21: Derivation of 0D blood flow models
A family of zero-dimensional (0D) blood flow models can be derived by integrating in space over the 1D equations.
1) Integral averages of the physical quantities of interest
with : the volume of the vessel compartment.
2) Mass conservation equation
where and .

## Slide 22: Derivation of 0D blood flow models
A family of zero-dimensional (0D) blood flow models can be derived by integrating in space over the 1D equations.
1) Integral averages of the physical quantities of interest
with : the volume of the vessel compartment.
2) Mass conservation equation
3) Momentum balance equation
Assumptions:
(A1) the contribution of the convective term is neglected;
(A2) the variation of with respect to is small compared to that of and , replacing with (or ).

## Slide 23: Derivation of 0D blood flow models
A family of zero-dimensional (0D) blood flow models can be derived by integrating in space over the 1D equations.
1) Integral averages of the physical quantities of interest
with : the volume of the vessel compartment.
2) Mass conservation equation
3) Momentum balance equation
resistance
inverse of inductance

## Slide 24: Derivation of 0D blood flow models
A family of zero-dimensional (0D) blood flow models can be derived by integrating in space over the 1D equations.
1) Integral averages of the physical quantities of interest
2) Mass conservation equation
3) Momentum balance equation
with
: inductance
: resistance
???

## Slide 25: 0D blood flow models
Again, we need to specify a constitutive law relating pressure and volume(area):
Simple linear relation , via : vessel wall compliance;
Nonlinear elastic relation (in arteries) , with : vessel wall stiffness (related to );
Nonlinear viscoelastic relation (in arteries) , with : viscoelastic parameter;
…
Similarly, model parameters ( and ) can be:
constant : and
time-/state-dependent : and .
Nonlinear vs linear dynamics,
Time-/space-/state-dependent vs constant parameters,
…
 Model sophistication for biological mechanisms and mechanical characteristics.

## Slide 26: How to use 0D models
Model reduction
1D  0D
One 0D lumped compartment with equivalent hemodynamic function
From micro- to macro-scale
More details in tomorrow’s lecture on multiscale modelling by G. Maso Talou!!!

## Slide 27: Comparing 0D & BG-0D models
Refreshing what we’ve learnt from P. Hunter’s lecture…

## Slide 28: Comparing 0D & BG-0D models
Refreshing what we’ve learnt from P. Hunter’s lecture…
A modular framework for CVS modelling
Integrated whole-body physiology models from cellular to organ and system levels

## Slide 29: 0D heart and valve models
Pressure-dependent source resistance
Time-varying elastance
Valve model

## Slide 30: Geometric multiscale
(mass conservation )
(continuity of –total– pressure)
0D models as BC to 3D models
Coupling 0D, 1D and 3D models to construct hetero-dimensional CVS models.

## Slide 31: Numerical schemes
99% of cases, we need numerical schemes to discretise and numerically solve our models, to predict the behaviour of the system.
0D models  ODEs
 time integration schemes
1D & 3D models  PDEs
space + time discretization
Finite Difference (FD) schemes,
Finite Volume (FV) methods (e.g., 1D),
Finite Element (FE) methods (e.g., 3D FSI),
…
⚠️ Some numerical challenges ⚠️
stability of the numerical methods and couplings;
convergence;
stiffness;
accuracy of the predicted numerical solution;
computational cost of simulations;
…

## Slide 32: What else?
Autonomic nervous system [rapid/short-term]
  Baroreceptors – ”top-down” systemic controller
  Chemoreceptors (O2, CO2, pH)
  Sympathetic activity (vasoconstriction)
Humoral/endocrine regulation [intermediate/long-term]
Local/autoregulatory mechanisms
  Cerebral autoregulation – local protective mechanism
  Metabolic control and myogenic response
Respiration
…
Notes: Control mechanisms to maintain BP, flow and tissue perfusion

## Slide 33: Context of Use – Brainstorm!
💡🤔 …what is your context of use then, and what CVS model do you need?

## Slide 34: PART III
Does one size fit all?
1.
Sensitivity Analysis Which parameters matter and drive model output?
2. Identifiability Analysis Can we determine them uniquely using the available data?
3.
Model Calibration Finding subject-specific parameter values
Filtering non-influential parameters
Refining parameters or data?
Subject-specific Digital Twin

## Slide 35: Model Calibration
Let’s define a model with inputs and parameters as
Experimental measurements are available, which relate to the model predictions as
where is the observation operator.
defines the post-processing of the model predictions to compare with the experimental data – It extracts features from the model outputs.

## Slide 36: Model Calibration
Find the parameters that for a given set of measurements satisfy
quantifies the disagreement between the model observations and the measurements.
impose restrictions to the model parameters, such as priors or constraints. Key for ill-posed problems or incorporating priors.
: regularization weight.
is the set of admissible parameters for the model. Note that constraints such as algebraic relationships between parameters, , can be modelled in the definition of this set (instead of as constraints in ).

## Slide 37: Model Calibration
Example of formulation for the data term
standard deviations to reduce bias towards observations with higher variability;
empirical weights to bias calibration towards the most reliable measurements.

## Slide 38: Sensitivity Analysis
Sensitivity analysis (SA) allows the identification of the parameter or set of parameters that have the greatest influence on the model output It provides useful insight into which model input contributes most to the variability of the model output.
Two types of SA:
  Local SA (OAT = one at a time): evaluates changes in the model outputs with respect to variations in a single parameter (while holding other parameters constant)
    Local sensitivity indices: .
  Limitation: the interaction between parameters cannot be evaluated.
  Global SA.

## Slide 39: Sensitivity Analysis
Sensitivity analysis (SA) allows the identification of the parameter or set of parameters that have the greatest influence on the model output It provides useful insight into which model input contributes most to the variability of the model output.
Two types of SA:
  Local SA.
  Global SA: all parameters are varied simultaneously over the entire parameter space, for the simultaneous evaluation of (i) the relative contributions of each individual parameter, as well as (ii) the interactions between parameters to the model output variance
    Sobol Indices
      : first‐order contribution from the -th input parameter to the output variance,
      : second‐order contribution from the interaction between the -th and -th parameters,
      …
      : total‐order sensitivity indices (overall effects of one parameter on the model output).

## Slide 40: (Local) Identifiability Analysis
Calibration yields a set of parameters that optimise the agreement with the observations and other constraints.
Are these the “unique” parameters that optimise/calibrate our model?
For a given model and experimental measurements with a given uncertainty (or noise), we analyse the reliability of the obtained optimal parameters .
Two main identifiability analyses:
Structural identifiability;
Practical identifiability.
Notes: *To a reasonable level of precision. Notice that highly noisy measurements will define a family of plausible parameters for the model, such that all predictions are within the bounds of the noise around the ground truth.

## Slide 41: (Local) Identifiability Analysis
Two main identifiability analyses:
Structural identifiability: analysis of the structure of the model , assuming infinite, continuous and noise free measurements .
Practical identifiability: analysis of the impact of the practical constraints related to (noise/uncertainty) and their impact on the uncertainty of the estimated
  Bayesian approaches (MCMC);
  Profile likelihood.
Notes: *To a reasonable level of precision. Notice that highly noisy measurements will define a family of plausible parmeters for the model, such that all predictions are within the bounds of the noise around the ground truth.
Practical identifiability: analysis of the impact of the practical constraints related to (noise/uncertainty) and their impact on the uncertainty of the estimated – the effect of the noise (uncertainty) in the measurements for the estimates of .
*To a reasonable level of precision. Notice that highly noisy measurements will define a family of plausible parmeters for the model, such that all predictions are within the bounds of the noise around the ground truth.
Practical identifiability: analysis of the impact of the practical constraints related to 𝐳 ̂ (noise/uncertainty) and their impact on the uncertainty of the estimated 𝜽 – the effect of the noise (uncertainty) in the measurements 𝐳 ̂ for the estimates of 𝜽.

## Slide 42: (Local) Identifiability Analysis
Decrease in complexity to ensure models can be calibrated to clinically available, subject-specific data.
Notes: *To a reasonable level of precision. Notice that highly noisy measurements will define a family of plausible parmeters for the model, such that all predictions are within the bounds of the noise around the ground truth.
Practical identifiability: analysis of the impact of the practical constraints related to (noise/uncertainty) and their impact on the uncertainty of the estimated – the effect of the noise (uncertainty) in the measurements for the estimates of .
*To a reasonable level of precision. Notice that highly noisy measurements will define a family of plausible parmeters for the model, such that all predictions are within the bounds of the noise around the ground truth.
Practical identifiability: analysis of the impact of the practical constraints related to 𝐳 ̂ (noise/uncertainty) and their impact on the uncertainty of the estimated 𝜽 – the effect of the noise (uncertainty) in the measurements 𝐳 ̂ for the estimates of 𝜽.

## Slide 43: Model Calibration
And now we can calibrate!
In our case:
:
:
:
:
:
:

## Slide 44: Model Calibration
And now we can calibrate!
In our case:
: CVS model;
: pressure, volume, flow rate in each model compartment at the current time step;
: elastic modulus of arterial walls, capacitance of venous compartments, resistance of arterial compartment, elastances of heart ventricles, total stressed blood volume, etc.;
: pressure, volume, flow rate in each model compartment at the next time step, i.e., ;
: systolic and diastolic pressure in the brachial artery, mean and max flow in the aortic root, predicted by the model;
: systolic and diastolic cuff pressure at the brachial artery level, and aortic root mean and max flow measured with Doppler ultrasound.

## Slide 45: Thank you!
Time for Q&As!
And our tutorial!

## Slide 46: Some useful references
L. Formaggia, A. Quarteroni, and A. Veneziani, Eds. “Cardiovascular Mathematics: Modeling and Simulation of the Circulatory System.” Vol. 1. MS&A: Modeling, Simulation & Applications. Milano: Springer, 2009. https://doi.org/10.1007/978-88-470-1152-6.
P. J. Blanco, and L. O. Müller. “One‐Dimensional Blood Flow Modeling in the Cardiovascular System. From the Conventional Physiological Setting to Real‐Life Hemodynamics.” Int J Numer Meth Biomed Engng, 41:e70020, 2025. https://doi.org/10.1002/cnm.70020.
B. Ghitti. “Numerical methods for computationally efficient and accurate blood flow simulations in complex vascular networks: Application to cerebral blood flow.” PhD Thesis. University of Trento, 2023.
B. Ghitti, E. F. Toro, and L. O. Müller. “Nonlinear lumped-parameter models for blood flow simulations in networks of vessels.” ESAIM: Mathematical Modelling and Numerical Analysis, 56(5):1579–1627, 2022. https://doi.org/10.1051/m2an/2022052.
A. Sharifzadeh-Kermani, J. Shen, F. Argus, et al. “Semi-automated pipeline for generating personalised cerebrovascular models.” Biomech Model Mechanobiol, 24:251–264, 2025. https://doi.org/10.1007/s10237-024-01908-5.
E.F. Toro. “Riemann Solvers and Numerical Methods for Fluid Dynamics: A Practical Introduction.” 3rd edn. Springer-Verlag Berlin Heidelberg, 2009.